## Slide 1: Simscape Tutorial
David S. Carabis
Rensselaer Polytechnic Institute

## Slide 2: Overview
Manipulator model (rigid joint):
Accounting for gearing/motor inertia:
What about friction?
  Adjust motor torque
Mass-inertia
Centrifugal/Coriolis
Gravitational
Motor torque
External spatial forces
Add gear ratio squared times motor inertia to diagonal elements of mass-inertia matrix
Note: assumes motors are 1D rotational elements
or

## Slide 3: Overview
What are we trying to do?
Forward dynamics: solve for given
Tools available:
  Euler-Lagrange
  Newton-Euler (order N3)
  Newton-Euler (recursive; order N)
  Simulation software (Simscape, MapleSim, DARTS, etc.)

## Slide 4: Method Comparison
Implementation time (my subjective opinion)
  Euler-Lagrange: time consuming; requires in-depth dynamics knowledge; symbolic matrices can be difficult to work with
  Newton-Euler: time consuming; requires in-depth dynamics knowledge
  Simulation packages: learning curve varies (Simscape is easy to learn; DARTS is difficult to learn); implementation is fast

## Slide 5: Method Comparison
Symbolic matrices available
  Euler-Lagrange: yes
  Newton-Euler: yes
  Simscape: no
Note: for larger DOF, symbolic terms often unintelligible
Example: can’t display centrifugal/Coriolis terms for 7 DOF robot without crashing Matlab

## Slide 6: Method Comparison
Run-time speed (Matlab/Simulink/Simscape)
  Euler-Lagrange: 30-60 seconds in Matlab to do symbolic substitution for a single state (rigid-joint arm); then, still have to invert
  Newton-Euler (order N): 65 s for 10 s simulation (flexible-joint robot; may be some Simulink overhead)
  Simscape: 28 s for 10 s simulation (flexible-joint robot)

## Slide 7: Method Comparison
Mathematical understanding (my subjective opinion)
  Euler-Lagrange/Newton-Euler: Good – both can provide symbolic and numerical models
  Simscape: No intuitive understanding

## Slide 8: Method Comparison
Visualization
  Euler-Lagrange/Newton-Euler: Need additional code
  Simscape: Included in software

## Slide 9: Method Comparison - Summary
Method | Euler-Lagrange | Newton-Euler | Simscape
Implementation Time | Requires good understanding of dynamics | Requires good understanding of dynamics | Learning curve; easy to implement after software is understood
Symbolic Matrices | Yes | Yes | No
Sim Time | Extremely slow | Fast | Fastest
Mathematical Understanding | Good | Good | Bad
Visualization | Need additional code | Need additional code | Included

## Slide 10: Method Comparison
Why bother with different methods?
  Confirm results (is code correct?)
  Obtain mathematical understanding
  Quick run-time
My recommendation:
  Symbolic/numerical comparison of EL/NE (single states)
  Simulation comparison of NE/Simscape
  Use Simscape for simulations and NE for mathematical understanding of model

## Slide 11: Building Model in Simscape
Consider robot:
Given: Kinematics
Link masses
Link COM
Link inertia Friction models

## Slide 12: Building Model in Simscape
Local frame for 2nd link in Simscape z axis aligned with rotation

## Slide 13: Building Model in Simscape
Tips:
  Keep frames that data is represented in in mind – may not be what is needed in Simscape model
  Keep rotation frames in mind – Simscape does NOT follow PoE convention
  Consistent ODE solver/step sizes for comparison (try fixed step first)
  Correct boundary conditions in NE

## Slide 14: Building Model in Simscape
Base (must connect to world frame)
Motor torque vector note must be converted to Simscape signal
Joint data – note that this must be converted to Simulink signal to save data
Transform from joint coordinate frame to Center of Link (e.g., center of cylinder if using cylinder shapes)
Transform Center of Link to next joint
Second link (keep repeating for higher DOF robot)

## Slide 15: Flexible Joint Model
Assumptions
  1D rotational inertia for motor
  No gyroscopic effect (motors are in inertial frame)
Model [Spong 1987]
Where to add gearing? Depends on experimental setup

## Slide 16: Flexible Joint Model
What about gyroscopic effects?
  Usually small
  For space manipulators with small floating bases, can be significant [Murphy 1993]
Dynamic model
Do NOT add motor inertias/gear ratios

## Slide 17: Flexible Joint Model
What gear ratio convention is being used?
Speed reducer/torque multiplier (N>1)
Note that direction switches with every gear We assume motor direction such that positive motion of motor/link is consistent

## Slide 18: Flexible Joint Model
How to implement in NE algorithm?
  Use same algorithm (without motor inertia/gearing terms in mass-inertia matrix)
  Set
  Solve motor dynamic based on current state ; can use Simulink blocks

## Slide 19: Building Flex Joint Model Simscape
Motor model see next slide
Motor torque
Joint – do not use internal spring/ damper as they do not include gear ratio
Joint data out
Transforms from joint coordinate frame to link center, link mass, and transform from link center to next joint coordinate frame (same as rigid joint example)

## Slide 20: Building Flex Joint Model Simscape
Motor model
Motor dynamics
Flexible joint model
Reaction torque from flexible joint

## Slide 21: Building Flex Joint Model Simscape
Motor dynamics
Flexible joint model
Motor position
Motor inertia
Motor torque
Reaction torque
Viscous damping
Flexible joint spring coefficient
Gear ratio
Link-side position
Coupled viscous damping

## Slide 22: Flexible Joint Model w/ Gyro
How to include gyroscopic effect?
  Use 1D rotational inertia for motor
  Will generate different results than NE algorithm presented earlier in the presentation
Motor reaction torque
Reaction torque

## Slide 23: Flexible Joint Model
Simscape
  What about built-in spring damper? Would get incorrect spring terms using this method